Remarks

- New lock is configured to grant any fingerprint or ID card access.

- The lock is equipped with mechanical keys for manual unlocking. Remove mechanical keys from the package and keep them in a safe place.

- To power up the lock, four alkaline AA batteries (not included) are required. Non-alkaline and rechargeable batteries are NOT recommended.

- Press the fingerprint sensor or the sensor holder to power up the lock. To avoid unlocking the door when pressing the fingerprint sensor, pressing the sensor holder to power up the lock is recommended.

- The operation of lock setting has a stand-by time limit of 10 seconds; if there is no any activity, the lock will shut off after 10 seconds.

- Keep your fingers clean when using this lock.

- To open door with ID card, you must press the sensor holder to power up the lock first.

- Administrator and other users can choose either fingerprint or ID card for enrollment and verification.

- Identity verification of administrator is required before enrolling other users. No matter which verification method administrator uses, other users can choose independently whether to enroll by fingerprint or ID card.

Appearance

Profile

User Introduction

| User Type | Capacity | Privilege |
| --- | --- | --- |
| Administrator | 20 (Fingerprint:10, ID Card: 10) | Add/delete fingerprint or ID card; Enable Normally Open (NO) mode; Unlock the door |
| Normal User | 120 (Fingerprint: 60, ID Card: 60) | Unlock the door; Enable NO mode |
| Temporary User | 40 (Fingerprint: 20, ID Card: 20) | Unlock the door; Enable NO mode |

Button Definition

| Buttons | Function | Other functions |
| --- | --- | --- |
|  | Add Users |  |
|  | Delete Users |  |
|  | Administrator User Group | Enable NO mode |
|  | Normal User Group | Enable NO mode |
|  | Temporary User Group | Enable NO mode |

Lock Status Indication

| Lock Status | Indication |
| --- | --- |
| Successful Operation | 1 beep and LED blinks in green |
| Failed Operation | 2 beeps and LED blinks in red |
| Low battery | 7 beeps and LED blinks in red for 7 times |
| Unlocking | 1 beep and electric engine makes a rolling sound for the first time, which indicates that the door is open. |
| Locking | Electric engine makes a rolling sound for the second time, which indicates that the door is closed. |

Lock Initialization

Method 1                                 Method 2

How to use mechanical key?

How to use 9V emergency battery?

Registering First Administrator

| Operating Steps |  | Indication |
| --- | --- | --- |

Registering Other Administrators

| Operating Steps |  | Indication |
| --- | --- | --- |

Registering Normal User

| Operating Steps |  | Indication |
| --- | --- | --- |

Registering Temporary User

| Operating Steps |  | Indication |
| --- | --- | --- |

Deleting Temporary User Group

| Operating Steps |  | Indication |
| --- | --- | --- |

Deleting Normal User Group

| Operating Steps |  | Indication |
| --- | --- | --- |

Deleting Admin Group

| Operating Steps |  | Indication |
| --- | --- | --- |

Enabling/Disabling Normally Open Mode

Enabling Normally Open Mode:

| Operating Steps |  | Indication |
| --- | --- | --- |

Disabling Normally Open Mode:

Press the sensor holder to power up the lock, and then place any registered finger or ID card 1 time to disable it.

# Text boxes

User Manual

ML10-ID

Version: 1.0

Date: Oct., 2015

1  LED

2  Fingerprint Sensor

3  Sensor Holder

4  ID Card Swiping Area

5  Handle

6  Mechanical Key Hole

7  Battery Box Cover

8  Battery Area

9  Button  / Temporary User

10  Button  / Admin user

11  Back LED

12  Button  / Delete user

13  Button  / Add user

14  Reset Button

15  Button  / Normal User

16  9V Emergency Battery Interface

1

7

8

9

10

11

12

13

14

15

16

2

3

4

5

6

Operating Steps

Operating Steps

Indication

Note: The lock will be restored to factory defaults after initialization, and the door can be opened with any fingerprint or ID card.

Hexagon Screw

Note:  1. The first user (fingerprint or ID card) will be the first administrator automatically in default setting.

2. Admin group supports 20 users (10 for fingerprints and 10 for ID cards); you can still register 19 new administrators in the next step.

3. The operating steps of registering new users: press button 1/2/3 to select user group, and then place one new finger 3 times on the fingerprint sensor or swipe a new ID card 1 time on the card swiping area for registration. You can continue registering new user afterwards.

Note: Admin group supports 20 users; you can still register 19 new administrators in this step.

Note: Normal user group supports 120 users (60 for fingerprints and 60 for ID cards).

Note: Temporary user group supports 40 users (20 for fingerprints and 20 for ID cards).

Note: Deleting operation is only valid for groups.

Note: Deleting operation is only valid for groups.

Note: Deleting operation is only valid for groups.